## Slide 1: Yield Tool Tutorial
Bijan Nemati
2/13/2016

## Slide 2: What does it primarily do?
The main calculations:
  Signal and noise
  Time to reach a given signal to noise ration (SNR)
  Margin and time for imaging and characterization of known RV planets
Implementation:
  Most recent version is in Excel
  Matlab version also exists and needs updating
    Can allow 2D dark holes in addition to the azimuthally averaged summaries used by the excel version

## Slide 3: What this tutorial aims to cover
Basic use cases of the tool
How to trace calculations
Some tricks in excel
  Named cells
  Lookup (vlookup, hlookup)
  Scenarios
  Data tables
  Conditional formatting

## Slide 4: Analytical Expression for SNR
Photometric SNR means we include planet shot noise
  Keep in mind that we are considering the post speckle-subtraction SNR
We write the total noise as:
The uncorrelated, random noise is given by:
  Note: This is the post-subtraction error, and should in principle reflect noise contributions for both the target and reference images. However, consistent with our assumption that the reference is significantly brighter than the target, we consider the error being dominated by the target star image only.
random,
uncorrelated, reduces with t
Speckle subtraction error, excluding measurement noise
photonic (shot noise) terms
planet
speckle
zodi
electronic terms
dark
clk. Ind. Chg.
read noise
planet signal
fraction of core light in region of interest for SNR
EMCCD excess noise factor

## Slide 5: Looking a little more closely at
The speckle subtraction term contains only the speckle instability effects.
  Excludes noise in the subtracted images, and corresponds to the post processing error
For a given level of speckle instability, different post processing schemes (e.g. PCA, KLIP) will have different dependencies on prior data.
But, in the context of a single observation, taking a total integration time t, this error grows at the same rate as the signal, i.e.,
A useful version of this parameterization defines a post-processing improvement factor, which can depend on many variables unstated here, that is calculated from the residual speckle scene according to:
NB: The above definition shows how is measured, not its dependencies!
From this definition, we have:
residual speckle, excluding shot noise;
spaced grid superimposed on top
is given by the rms of the residual intensity variations after averaging within each sized pixel
mean raw speckle rate

## Slide 6: Putting it all together: time to reach SNR
Analytical expression for SNR:
Speckle Subtraction Error:
Time to reach desired SNR:
mean speckle rate
IWA ~ 3 l/D
OWA
Dark Hole
ROI
noise rate
planet rate

## Slide 7: Conversion Efficiency
Electron at pixel
Electron at amp
Incident photon
Counted electron
QE
CTE
use to estimate shot noise
use to compute signal
conversion
efficiency
Fraction of photons counted to photons incident on the sensor
QE
CTE

## Slide 8: Requirement on Total Noise
What are the noise variance contributors for the detector at the end of mission, in a single frame, and a single pixel?
Dark noise variance
CIC noise variance
Read noise variance
Example: EMCCD

## Slide 9: WFIRST Coronagraph Detector Requirements
The basis of these requirements is the already-achieved end of life EMCCD performance, as well as a detection and characterization SNR model.
The following conditions must be applied when evaluating detectors against these requirements:
  Detector is at the end of life for the WFIRST mission (6 years at L2)
  Incident flux from all photon sources is e-/pixel/frame
  Detection is in the photon counting mode
  The detector is no colder than -105oC or 168 K
Conversion Efficiency Defined as the fraction of times a single incident photon is counted as a single photon and includes
  Quantum Efficiency
  Charge transfer efficiency (where applicable)
  Photon counting efficiency (thresholding efficiency)
Total Noise from one pixel in a 100s frame Defined as the standard deviation of the combined detector noise contributions from:
  Read noise
  Dark current
  Clock induced charge (CIC, where applicable)
Conversion efficiency | Imaging 1 | Imaging 2 | IFS 1 | IFS 2
 | 450 nm | 565 nm | 660 nm | 770 nm
 | 10% | 10% | 18% | 18%
@ | 23% | 24% | 23% | 18%
Conversion efficiency | Imaging 1 | Imaging 2 | IFS 1 | IFS 2
 | 450 nm | 565 nm | 660 nm | 770 nm
 | 10% | 10% | 18% | 18%
 | 23% | 24% | 23% | 18%
Combined Noise | 1 pixel, 100s frame, at
 | 0.27 e-
Combined Noise | 
 | 0.27 e-

## Slide 10: Calculating Planet Yield

## Slide 11: A Simple Observing Scenario for Yield
We seek a simple analytical model of planet yield, via calculating the time to reach a desired SNR
We need to be explicit about the observing assumptions
We choose these assumptions:
  We are after a photometric measurement
    Though note that in detection, we would not be doing photometry. The SNR is different in that case.
  We are doing differential imaging.
    The SNR is the post-differential imaging SNR.
    For simplicity we assume we are doing Reference Differential Imaging (RDI).
  The reference star is brighter than the target star
    If between target and reference then
    Shot noise of reference speckles is small compared with shot noise of target speckles
    There is a normalization step also
  Exo-zodi is smooth and extended for both stars
    Brightness distribution structures are >> lam/D
Target
Reference
Tar – Ref
(RDI)

## Slide 12: Aside: Distinguishing types of SNR
For spectrometry, with the IFS, we are interested in the photometric SNR:
For planet detection, with the imager, we would be interested in detection SNR:
  The noise of interest in this case does not include the signal’s shot noise
  We are instead interested in the background’s false positive probability
Detection and spectroscopy are different statistical questions.
planet signal
background

## Slide 13: Noise Equivalent Contrast (NEC):
What is the minimum planet contrast that can be seen with SNR 5 under our observing scenario?
Equivalent Contrast Definition:
  The planet that will be detected with SNR of 𝑺 after integrating for time t is one which has a planet-contrast equal to the S-𝝈 equivalent contrast, after post processing:
How dim a planet can be seen with SNR = S ?
R
T
This conversion factor is set by the scenario parameters
Planet signal in the core region after t seconds
area
thruput
QE
time
flux
signal
fraction

## Slide 14: Asymptotic Behavior of
How does the NEC depend on post processing and integration time?
For imaging, , so for simplicity we drop this factor, and we have:
For very short times the first term dominates and there is no benefit from post-processing
At large times, the first term under the radical drops out, so that we arrive at:
t
dominated; not much benefit
from post-processing
Our definitions of NEC: