## Slide 1: WFIRST Coronagraph Photometry and Yield for Planet Imaging
Bijan Nemati
9/23/2016

## Slide 2: Introduction
A simple analytical approach to calculating SNR and time to achieved a given SNR is presented.
This includes a detailed look at the categories of throughput loss contributions to the planet signal and to the background
Also included, for WFIRST coronagraph, is a detailed description of key quantities tabulated in John Krist’s contrast tables.
The presentation concludes with the time and SNR equations and example calculations.

## Slide 3: Signal and Background Contributions
The signal is taken as the excess within the PSF core.
The PSF core is defined to be the area bounded by the footprint of the PSF contour at FWHM.
We would like to consider three contributions:
  Signal
  Star (speckle) Background
  Zodi Background
speckles
planet
PSF core
zodiacal dust

## Slide 4: Coronagraph Throughput Contributions
FSM
Collimator Bench
DM2
FocM
R1 OAP1
R1 OAP2
Pupil mask
Lyot
mask
Filter
wheel
Field stop
mask
to LOWFS
PBS
M4
M3
COR F1
R3 OAP1
R3 OAP2
COL F1
COL F2
FS OAP1
FS OAP2
Coronagraph Bench
R2 OAP1
R2 OAP2
DM1
FM
IFS/Img Selector
Focal Plane mask
Radiation Shield Mirror
FPA
Telescope
T1
T2
COR F2
From SNR repository rev 422: 20160406 Nemati Rates for Typical Observation.sm

## Slide 5: Coronagraph Contrast
The Coronagraph contrast is computed on a per pixel basis.
Steps to getting contrast at
  Propagate a flat wavefront (corresponding to the star being at 0,0) through the optical system, from the primary all the way to the imager
  Obtain the intensity distribution in the focal plane
    Normalize the intensity distribution to the total incident power (photons/second) incident on the unobscured parts of the primary.
  Repeat with a tilt applied to the incoming wavefront so that the star is effectively at  this gives
  Divide the intensity distribution in step 2 by the PSF peak in step 3
IWA ~ 3 l/D
OWA
Dark Hole with Speckle
(u,v)
(0,0)
source
evaluate

## Slide 6: Using the Coronagraph Contrast Tables
The HLC polx and PIACMC tables include the attenuation (throughput loss)
due to the polarizer for I, core_thruput, PSF_peak, and occ_trans
so, to calculate the mean speckle level, the throughput
Below are excerpts from two contrast table files for the HLC design
---------------------------------------------------------------------------------------------------------------------------
r(lam/D) r(arcsec) I contrast core_thruput PSF_peak area(sq_arcsec) occ_trans
---------------------------------------------------------------------------------------------------------------------------
............. hlc_20140623-139_0.4mas_jitter_results.txt ................................................................
3.00000 0.143602 1.1689422e-11 3.8758899e-09 0.022367177 0.0030159324 0.0020705070 0.39442343
3.30000 0.157962 6.6227517e-12 1.5575568e-09 0.030859951 0.0042520129 0.0020109240 0.39442343
5.40000 0.258484 4.5271587e-12 7.9960251e-10 0.041660457 0.0056617615 0.0020556112 0.39442343
............. hlc_20140623-139_0.4mas_jitter_results_polx.txt ...........................................................
3.00000 0.143602 1.6973625e-12 1.1255972e-09 0.011183589 0.0015079662 0.0020705070 0.19721172
3.30000 0.157962 1.5311561e-12 7.2020295e-10 0.015429976 0.0021260064 0.0020109240 0.19721172
5.40000 0.258484 1.1051182e-12 3.9037963e-10 0.020830229 0.0028308807 0.0020556112 0.19721172
...........................................................................................................................
Reductions due to reflections, CCD QE are omitted. Coronagraph mask throughputs
are included. Polarizer reduction is included as noted below.
> I = mean speckle intensity at r, normalized to flux incident on primary
> contrast = I(r) / PSF_peak(r)
> core_thruput = fraction of light incident on primary that makes it into the FWHM region of a field PSF centered at r
> PSF_peak = fraction of light in peak pixel of field PSF centered at r normalized to flux incident on primary
> area = area of the FWHM region of the field PSF centered at r
> occ_trans = occulter * lyot stop transmission at r
> Pixel sizes (for I, PSF_peak): hlc, piaacmc = 0.3 lam/D, spc = 0.2 lam/D
> Reduction by 0.5 due to polarizer included in HLC polx and piaacmc values for: I, core_thruput, PSF_peak, and occ_trans
...........................................................................................................................
Documentation in setupAFTA.m

## Slide 7: Planet Contrast
Planet contrast is independent of the instrument. It is simply the ratio of the flux arriving at the instrument aperture from the planet divided by the same from the star.
% Planet contrast C = albedo * phi(alpha) * (r_p / SMA)^2;
% phi(alpha) = (sin(alpha) + (pi-alpha)*cos(alpha)) / pi , where alpha = phase angle
Traub & Oppenheimer
albedo
Phase law
Observer
Exo system
planet
LOS
used
(simple case of 90 deg inclination angle shown)

## Slide 8: Attenuation Factors and Throughput
Because of the way the coronagraph contrast is defined, the following differences apply to the photometric attenuation factors for planet, speckle and zodi:
HLC Pol-x Example
X Needs to be included separately: it is not in the contrast table
Core throughput
 | Obsc | Reflec | Occulter | PSF | Filter | Polariz
Planet | X | X | X | X | X | X
Speckle | X | X | 1 | 1 | X | 1
Zodi | X | X | X | 1 | X | X
For example, when calculating the mean speckle level, we start with John Krist’s contrast, and apply losses from obscuration, all the reflections, and the filter. Some of the contrast tables (e.g. PIAA and HLC non-Pol-x) do not include polarizer effect so for those another factor of ~0.5 must also be applied.
So we can use this table to get the various throughputs:

## Slide 9: Important metric: Requisite time to reach SNR
Analytical expression for SNR:
Can invert the equation to get the requisite time to get to a desired SNR:
photonic (shot noise) terms
electronic terms
where
planet rate:
fraction of core light in region of interest for SNR
there is also a spatial term, the confusion noise arising from the residual speckle structure
mean speckle rate
Temporal noise rate
planet
speckle
zodi
dark
clk. Ind. Chg.
read
IWA ~ 3 l/D
OWA
Dark Hole with Speckle
(u,v)
(0,0)

## Slide 10: Detector Pixels in the IFS Configuration
For the IFS, the SNR region of interest (ROI) comprises the collection of pixels that altogether are involved in the photometry of a single spectral element
Collimator
Compound
Prism
Camera
Lenslet Array
WFIRST Coronagraph
IFS (PISCES)
Imager plane
SNR
ROI
spectral direction
‘spatial’
direction
one lenslet spectrum
PSF spectrum
IFS Detector
PSF
The system is constant-dispersion, therefore the sampling in the spectral dimension is set, and not wavelength dependent.

## Slide 11: Another Correction: Differential Imaging
The factor fpp assumes speckles are somehow estimated
This estimation will bring with itself some errors – both random and systematic
For the random errors, this means there will be an extra contribution to noise
The simplest way is to assume a separate reference measurement (a la RDI) gives the speckle background.
Angular differential measurement (ADI) would have a similar error.
Either way, this means doubling of the variance for all terms except the signal shot noise
The noise rate would change to:
Target
Reference
Tar – Ref
(RDI)
for the random background
However, if there is a library of reference images, it is possible that this factor of 2 would not apply.

## Slide 12: Equivalent Contrast
Using the earlier slide’s definitions:
Equivalent Contrast Definition:
The planet that will be detected with SNR of after integrating for time t is one which has a planet-contrast
equal to the S- equivalent contrast. The signal for such a planet is given by:
It might be helpful to factor the equations a little differently to see how the SNR improves with time.
Consider the noise variance, which can be broken up into temporal and spatial terms:
For imaging, , so for simplicity we drop this factor, and we have:
Due to the statistical nature of the data that goes into achieving , it is implicitly a function of time, so we really can write it as For short integration times, we can expect to be decreasing (random errors) while for long times drifts will cause it to flatten or even increase.
For very short times the first term dominates and there is no benefit from post-processing
At large times, the first term under the radical drops out, so that we arrive at:
We are typically interested in the case , so we talk about the equivalent contrast.
t
dominated; not much benefit
from post-processing
Here, absorbed A and into

## Slide 13: Example Calculation: Planet Signal
The planet signal is calculated by starting with the planet contrast and applying the attenuation from PSF core fraction

## Slide 14: Example Calculation: Speckle Background

## Slide 15: Example Calculation: Zodi Background
Zodi background is an extended source
The PSF core fraction does not apply to Zodi

## Slide 16: Aside: Distinguishing types of SNR
Detection and spectroscopy are different, statistical questions.
For planet detection, with the imager, we would be interested in detection SNR:
For spectrometry, with the IFS, we are interested in the photometric SNR: