## Slide 1: WFIRST CGI Detector Radiation Environment
2017–01-31
Michael Cherng & Patrick Morrissey
Jet Propulsion Laboratory
©California Institute of Technology, Government sponsorship acknowledged

## Slide 2: Outline
L2 Radiation Environment
  6 year mission in an L2 orbit
  Solar flare protons
  Galactic Cosmic Rays (GCR)
Radiation Transport Calculation
2

## Slide 3: L2 Orbit
The relative location of the L2 point with respect to the Sun and Earth
Figure 2. Sun, Earth, and L2 Point

## Slide 4: L2 Radiation Environment
The dominant radiation source is solar protons from Solar Energetic Particle Events (Solar Flares)
Protons fluence from Galactic Cosmic Rays (GCRs) is 3 order of magnitudes lower than solar protons
4

## Slide 5: LEO vs L2
 | E>10MeV Trapped and Solar Protons | E>10MeV GCR
 | 7 year fluence (p-cm-2) | 
HST | 1.13e11 | 2.8e8
L2 | 6.48e11 | 9.8e8
HST Orbit
2
4
6
L2 Orbit@235Re
Lunar Orbit@60Re
HST and CGI are in very different environments

## Slide 6
Feynman 2002
(35 years of data)
10 Largest
Observed Flares
Log-normal Model
Distribution
~68 flares in 7 years

## Slide 7
7 years
3 years
5
Most L2 CCD damage will likely result from just 1-5 flares in a solar cycle, and these flares may occur any time during the 7-year active period.
How conservative is the test level?
Half empty or half full?
95% confidence
98% confidence

## Slide 8: Range of Protons in Matter
Mewaldt 2005
GCR
Solar
Nominal Shielding

## Slide 9: Radiation Level Calculation
Estimate the L2 environment using validated code
  JPL 91 Solar Proton Model
  Specify total fluence spectrum over lifetime [particles/cm2]
Simulate radiation exposure of detector using radiation transport code
  Displacement Damage Dose (DDD)
  Total Ionizing Dose (TID)
9

## Slide 10: Radiation Code Comparison
Solar Proton Code Cross Check
Predictions of solar protons at L2 for WFIRST and JWST were compared
WFIRST (JPL model at 6 yrs)
JWST (GSFC model scaled to 6 yrs)
Independent models
10

## Slide 11: Summary of Radiation Analysis
Radiation transport code NOVICE used to predict DDD and TID in L2
Direct insertion orbit, i.e. trajectory through Earth’s trapped-particle rad belts is inconsequential
  Soar proton model run at 95% confidence level
  Code was run for a range of camera shielding materials/thicknesses to in form choice of maximum test exposure
  Performance after mission life exposure was used to optimize shielding material/thickness
Code predicted cumulative TID of only 1 krad with 1 mm glass window
  => DDD is the major hazard
Aperture for image light
Fold Mirror
Camera package
Harding & Demers, et al. (2016)
11
Phase I (RT)
Phase II (Cryo)

## Slide 12: Limits of Shielding
Chart: Radiation Shield Thickness [mm]
| 3 | 5 | 10 | 15 | 20
Aluminum | 6765641569.4592 | 5174973488.8653 | 4135737009.544
Tantalum | 6129374337.2216 | 4199363732.7678 | 2163308589.6076 | 1620000000 | 1080000000 | 1000000000 | 932000000
  Two devices irradiated to this fluence
Data from analysis by Michael Cherng JPL Internal Memo 5132-15-015, 18 March 2015 & recent results July 2016
End of Life (EOL) DDD Exposure [10 MeV protons/cm2]
Test at RDF = 2 per JPL Flight Practices
12